## Slide 1
Astra
Simulator Briefing

## Slide 2: Astra Flight Tasks − Main Menu
Simulator Safety
X
LAHSO/ SMCGS
Presentation
Stall Video
Ground
Operations
Approaches
& Landings
Takeoffs
Systems
Maneuvers
Initial/Recurrent

## Slide 3: Astra Flight Tasks − Ground Operations
Taxi Operations
Abnormal Starts
Normal Start

## Slide 4: Astra Flight Tasks − Takeoffs
Windshear During Takeoff
Engine Failure During Takeoff
Rejected Takeoff
Normal Takeoff & Climb
Standard Takeoff
Procedure
Standard Takeoff
Briefing

## Slide 5: Astra Flight Tasks − Maneuvers
Mach Tuck
Demonstration
Dutch Roll Demonstration
Unusual Attitude
Recovery
Stall Recovery:
High Altitude
Approach to Stall: Landing Configuration
Approach to Stall: Takeoff with Partial Flaps
Approach to Stall: Clean Configuration
Steep Turns
Pitch Change Characteristics

## Slide 6: Astra Flight Tasks − Approaches & Landings
Windshear During Approach
Landing with
Pitch Mistrim
No-flap or Nonstandard
flap Approach
Missed Approach - OEI
Visual Approach
Circling Approach
Precision Approach - OEI
Rejected Landing
Non-precision Approach/CDFA
Missed Approach from Precision
Normal Landing
Precision Approach

## Slide 7: Astra Flight Tasks − Systems
Emergency
Evacuation
In-Flight Fire & Smoke Removal
Rapid Decompression
& Emergency Descent
Flight Controls
Fire Detection & Extinguishing
Environmental
Hydraulic
Electrical
Fuel
Anti-ice/De-ice
Navigation & Avionics
Engine Failure
(Shutdown & Restart)

## Slide 8: Simulator Safety Resources
Telephone:
Dial 147
for Simulator
Technician

## Slide 9: Simulator Safety Resources
Facility Fire Alarm
  (Strobe only, no audible alarm in the simulator.)

## Slide 10: Simulator Safety Resources
Fire Extinguisher

## Slide 11: Simulator Safety Resources
Emergency Hydraulic Cutoff Switch
(Make sure you don’t hit it accidentally if you pick up a checklist or iPad laying behind the pedestal.)

## Slide 12: Simulator Safety Resources
Rope Ladder

## Slide 13: Engine Start – Normal
Fuel controller: NORM
Standby pump: AUTO – “FUEL PRESS” light out – ON
Start switch: START
At minimum 10% N2 and positive N1 indication:
    Thrust lever – idle
    Ignition light – observe on
    Fuel flow – observe positive indication (300 pounds or less)
    Oil pressure light – should be out within 10 seconds
    ITT – monitor rise, observe limitations
    Ignition light – out at 50% N2 to indicate automatic start termination
Engine instruments: checked
Standby pump: select AUTO
Fuel controller: manual mode check

## Slide 14: Engine Start – Abnormal
Thrust Lever: Cutoff
Start Switch: STOP if ITT is less than 400C
Decide whether to motor engine or not:
  If you need to clear engine of fuel – motor for 15 seconds
  If you need to reduce ITT to below 400C – motor as necessary
  If it is a mechanical problem (no N1, no oil pressure) – DO NOT MOTOR
Starter Duty Limits:
  15 seconds on – 2 minutes off
  15 seconds on – 2 minutes off
  15 seconds on – 20 minutes off

## Slide 15: Taxi Operations
Taxi checklist should not interfere with looking outside and situational awareness.
Heads-down tasks should be performed by right-seat pilot while left-seat pilot is controlling tiller and looking outside.
Tasks which require high power settings should be deferred until stopped with parking brake set, away from the parking ramp/apron.
Visually clear all intersections along taxi route, monitor taxiway signs, and be aware of “hot spots” (locations with a history of potential risk of collision or runway incursion, and where heightened attention by pilots is necessary).

## Slide 16: Standard Takeoff Briefing
Before 80 knots:
    Reject for any malfunction
From 80 knots to V1 reject for:
    Any fire
    Engine failure
    Loss of directional control
    Thrust reverser deployment
    Runway obstruction
At or after V1:
    Continue takeoff

## Slide 17: Standard Takeoff Procedure
Pilot Flying:
    Ensure that all checklists are complete and aircraft is safely configured for takeoff:
      Flaps
      Ground Airbrakes
      Reversers
      Flight Airbrakes
      Trims
    Left hand on nose wheel tiller, right hand on thrust levers
    At 90 knots, left hand is moved to the yoke
    At V1 right hand is moved to the yoke
    Rotate approximately 2° per second toward 14° to 16°
    Once aircraft is at desired pitch, “pitch sync” command bars
    Maintain V2 +10 minimum until 400 AGL and clear of obstacles, then call for flaps to be retracted and an appropriate flight director mode
    Set climb power

## Slide 18: Standard Takeoff Procedure
Pilot Monitoring:
    Confirm power set to takeoff N1
    Maintain forward yoke pressure and crosswind correction
    At beginning of airspeed scale (60 KIAS) announce “Airspeed alive and cross-checked” if both indicators agree
    At 90 knots announce “90 knots”
    At PF command, relinquish yoke and continue to monitor
    When airspeed reaches V1 announce “V1”
    When airspeed reaches VR announce “rotate” or “VR”
    When visual and gauge indications show positive rate of climb, announce “positive rate”
    Retract landing gear when directed, immediately select yaw dampener ON and thrust reversers OFF
    At 400 AGL, announce “400 feet”
    At V2+10 minimum, 400 AGL minimum, and clear of obstacles, retract flaps and perform after-takeoff checklist when directed

## Slide 19: Standard Takeoff Procedure

## Slide 20: Takeoff: Declared Distances
Takeoff Run Available, Takeoff Distance Available, and Accelerate-Stop Distance Available should be considered for all takeoff planning.

## Slide 21: Normal Climb
Climb Profiles:
  Normal climb:
    Below FL300: 240 KIAS
    FL300 until 0.66M: 240 KIAS
    Then maintain 0.66M to desired altitude
  High-speed climb:
    Sea level to 10,000: 250 KIAS
    10,000 to FL250 or until 0.72M: 275 KIAS
    Then maintain 0.72M to desired altitude
    Rule of thumb for N1:
      Below 5,000 feet: N1 95 %
      Below 10,000 feet: N1 97 %
      Before or at 15,000: as charted

## Slide 22: Rejected Takeoff Briefing
Before 90 knots:
    Reject for any malfunction
From 90 knots to V1 reject for:
    Any fire
    Engine failure
    Loss of directional control
    Thrust reverser deployment
    Runway obstruction
At or after V1:
    Continue takeoff

## Slide 23: Rejected Takeoff Actions
Pilot Monitoring Actions:
  Call “ABORT ABORT ABORT” (and state problem if time permits)
  When PF brings thrust levers to idle, deploy ground airbrakes
  Forward pressure on yoke
  Notify ATC
  Airspeed calls during deceleration
Pilot Flying Actions:
  Both thrust levers to idle
  Maximum braking
  Thrust reversers as required
  Steering as required
  Maintain directional control

## Slide 24: Rejected Takeoff

## Slide 25: Engine Failure During Takeoff
Engine Failure (Above V1):
  Continue takeoff & state the failure (either pilot)
  Max thrust
  Establish directional control before rotation
  At VR rotate approximately 11° – 12° and pitch sync
  Retract landing gear when positively airborne
  Pilot Flying should call for heading mode and rudder trim as necessary
  Maintain V2 until 400 AGL minimum & clear of obstacles
  Accelerate to V2 +10 knots
  Flaps up at V2 +10
  Accelerate to VFS then retract slats
  Continue climb & accomplish Emergency, then Abnormal, then Normal checklists

## Slide 26: Engine Failure During Takeoff

## Slide 27: Windshear During Takeoff
Prior to liftoff:
  Recognize:
    Surrounding weather & reports (LLWAS, ATC, or other aircraft)
    15 – 20 knot fluctuation in airspeed
    Stagnate airspeed during takeoff roll
    Slow or longer than normal takeoff roll
  React:
    Considerations for abort:
      Available stopping distance
      Obstacles on departure path
      Higher than normal pitch to liftoff
      Delaying rotation?
      Rotation should begin no later than 2000 feet remaining
  Report:
    Advise ATC of deviations

## Slide 28: Windshear During Takeoff
After liftoff:
  Recognize:
    15 – 20 knot fluctuation in airspeed
    Abnormal vertical speeds
    Callouts from pilot monitoring
    Visual clues of climb
  React:
    Verify maximum power (APR?)
    After liftoff pitch to 15° and do not decrease
    Pitch to maintain positive climb or stop a descent
    Relax back pressure at stall buffet
    Pitch not to exceed 25°
    Do not change configuration until sustained climb and 1000 feet above obstacles
  Report:
    Advise ATC of deviations

## Slide 29: Trim & Pitch Change Characteristics
Trim for straight & level hands-off
For this maneuver try with and without pilot inputs:
    Increase power
    Decrease power
    Extend slats and flaps
    Retract slats and flaps
    Extend landing gear
    Retract landing gear
    Extend flight airbrakes
    Retract flight airbrakes
Note aircraft reaction to changes

## Slide 30: Steep Turns
Two turns:
  At least 180° of turn
  45° of bank
  250 knots
  Thrust approximately 80 to 85% N1
  Pitch approximately 2½° nose up
  Roll out 10° prior to desired heading
  Transition directly to opposite direction turn
Acceptable performance:
  Altitude ± 100 feet
  Airspeed ± 10 knots
  Heading ± 5°
  Bank angle ± 5°

## Slide 31: Stall Recovery: Clean Configuration Approach to Stall with Only Idle Thrust (Demo)
Beginning the maneuver:
  Thrust – idle
  Flaps – 0°
  Gear – up
  Autopilot – off or on
  Stall buffet
Recovery:
  Autopilot – ensure disengaged
  Pitch angle – lower to reduce angle of attack
  Bank angle – wings level
  Flight airbrakes – ensure retracted
  After demonstrating recovery solely by lowering the nose to reduce AOA:
  Thrust lever – max thrust
  After airspeed increasing and no stall buffet:
  Pitch attitude – adjust to return to desired flight path
Completion of maneuver:
  Return to assigned altitude and airspeed

## Slide 32: Stall Recovery: Clean Configuration En-route Stall with Idle Thrust & Autopilot On
Beginning the maneuver:
  Thrust – idle
  Flaps – 0°
  Gear – up
  Autopilot – off or on
  Stall buffet
Recovery:
  Autopilot – ensure disengaged
  Pitch angle – lower to reduce angle of attack
  Bank angle – wings level
  Thrust lever – max thrust
  Flight airbrakes – ensure retracted
  After airspeed increasing and no stall buffet:
  Pitch attitude – adjust to return to desired flight path
Completion of maneuver:
  Return to assigned altitude and airspeed

## Slide 33: Stall Recovery: Clean Configuration

## Slide 34: Stall Recovery: Takeoff with Partial Flaps
Beginning the maneuver:
  Flaps – 12°
  Gear – up
  Autopilot – on or off
  Climbing turn at 15° to 30° bank
  Thrust – 55% to 60%
  Stall buffet
Recovery:
  Autopilot – ensure disengaged
  Bank angle – wings level
  Pitch angle – lower to reduce angle of attack
  Thrust lever – max thrust
  Flight airbrakes – ensure retracted
  After airspeed increasing and no stall buffet:
  Pitch attitude – adjust to return to desired flight path
Completion of maneuver:
  Return to assigned altitude/heading/airspeed/departure procedure
  Initiate flap retraction at a minimum airspeed of V2 +10 knots

## Slide 35: Stall Recovery: Takeoff with Partial Flaps

## Slide 36: Stall Recovery: Landing Configuration
Beginning the maneuver:
  Established on precision approach, fully configured inside FAF:
    Gear – down
    Flaps – 40°
    Autopilot engaged, LOC and GS captured
  When below 1000 AGL, reduce thrust to less than what would be required to maintain VREF (for example, set 55% N1)
Recovery:
  Autopilot – ensure disengaged
  Pitch angle – lower to reduce angle of attack
  Bank angle – wings level
  Thrust lever – max thrust
  Flight airbrakes – ensure retracted
  Flaps – 20°
  As engines accelerate and no stall buffet:
  Pitch for positive rate of climb then retract gear
Completion of maneuver:
  Initiate missed approach procedure and advise ATC
  Initiate flap retraction with a minimum airspeed of V2 +10 knots

## Slide 37: Stall Recovery: Landing Configuration

## Slide 38: Stall Recovery: High Altitude
Beginning the maneuver:
  Altitude – near max operating for weight and temperature conditions
  Thrust – as necessary, establish climb
  Flaps – 0°
  Gear – up
  Autopilot – on
  Stall buffet
Recovery:
  Autopilot – ensure disengaged
  Pitch angle – lower to reduce angle of attack, pitch down as necessary to sacrifice altitude for airspeed
  Bank angle – wings level
  Thrust lever – max thrust (observe limitations)
  Flight airbrakes – ensure retracted
  After airspeed increasing to normal cruise speed and no stall buffet:
  Pitch attitude – adjust to return to desired flight path
Completion of maneuver:
  Establish level flight at normal cruise speed at a safe altitude

## Slide 39: Recovery from Unusual Attitudes
Nose high:
  Max thrust
  Bank 60° to 90° in the shortest direction
  Maintain bank until the nose approaches the horizon
  Roll wings level
  Allow airspeed to build to safe speed
Nose low:
  Reduce thrust to idle
  Roll wings shortest direction to level
  Deploy flight airbrakes (delay until less than 90° of bank)
  Raise nose to the horizon
  Retract flight airbrakes
  Establish a safe airspeed

## Slide 40: Precision Approach
Outside IAF:
    Set approximately 60% N1, adjust as necessary
    Slats down
    Airspeed 180 knots
    Complete descent and approach checks
Procedure turn outbound or base:
    Flaps 12°
    Speed 160 knots (VREF +30 knots)
    Facility tuned and identified
Localizer intercept:
    Flaps 20° (VREF +20 knots)

## Slide 41: Precision Approach
Approaching the final approach fix:
    One dot below glide slope: gear down, before landing checklist
Final approach fix:
    Glideslope intercept: flaps 40°
    Allow airspeed to gradually reduce to (VREF +½ gust)
Landing assured:
    Flaps 40° (VREF +½ gust)
    Autopilot and Yaw Damp disengaged

## Slide 42: Precision Approach

## Slide 43: Normal Landing
Maintain a constant rate of descent
Reduce power to idle before touchdown (at 50 feet)
Trim may be used during flare
Lower the nose wheel to the runway before elevator control is lost
Use thrust reverse to idle deploy (or more if required)
Brake as necessary
At 80 knots, the left seat pilot controls nose wheel steering
Pilot with yoke holds wind correction

## Slide 44: Landing: Declared Distances
Landing Distance Available should be considered for all landing runway planning. LDA may be less than total runway length due to displaced thresholds.

## Slide 45: Missed Approach
Go-around:
  Immediately and simultaneously
    Select go-around mode on flight director
    Pitch to command bars, maintain VREF minimum
    Thrust to max (stop descent)
  Establish climb VLC (around VREF)
  Flaps 20°
  Positive rate – gear up
  Flaps 12
Climb:
  At 400 feet AGL (minimum) and VREF +10 knots: flaps up
  Select appropriate flight director mode (HDG, NAV)
  Initiate missed approach procedure and advise ATC
  Accelerate to VFS / VAPP then slats up
Complete missed approach checklist

## Slide 46: Missed Approach

## Slide 47: Non-Precision Approach
Outside IAF:
  Airspeed 180 knots
  Complete descent and approach checks
Procedure turn outbound or base:
  Flaps 12°
  Speed 160 knots (VREF +30 knots)
  Facility tuned and identified
Course intercept:
  Flaps 20° (VREF +20 knots)

## Slide 48: Non-Precision Approach
Approaching the final approach fix:
  About 2 miles from FAF: gear down, Before Landing checklist
Final approach fix:
  Start clock (if a timed approach)
  Descend to MDA
  Flaps remain 20°
  VREF +10 knots = for straight in approach
  VREF +20 knots = for circling approach
Landing assured:
  If required, flaps 40° (VREF +½ gust)
  Complete before landing checklist

## Slide 49: Non-Precision Approach
  Advisory Circular 120-108 recommends use of a Constant Descent Final Approach (CDFA) technique for all non-precision approaches:
  A stabilized approach is a key feature to a safe approach and landing. It means maintaining a stable approach speed, descent rate, vertical flightpath, and configuration to the landing touchdown point. Depart the FAF configured for landing and on the proper approach speed, power setting, and flightpath, and at a rate of descent no greater than 1,000 FPM, unless specifically briefed.
  CDFA is a technique for flying the final approach segment of an NPA as a continuous descent. The technique is consistent with stabilized approach procedures and has no level-off. A CDFA starts from an altitude/height at or above the FAF and proceeds to an altitude/height approximately 50 feet (15 meters) above the landing runway threshold or to a point where the flare maneuver should begin for the type of aircraft being flown.
  CDFA should be used in place of the practice commonly referred to as “dive and drive,” which can result in extended level flight as low as 250 feet above the ground and shallow or steep final approaches.
  See illustrations on the following slides…

## Slide 50: Non-Precision Approach
The following figures show both NACO and Jeppesen examples of the VOR 22L approach at KJFK comparing “dive and drive” (red) and CDFA (yellow) flightpaths:
NACO Examples
Jeppesen Examples

## Slide 51: Non-Precision Approach
Note that this approach has a published descent angle of 3.14º. Use a table provided by the chart publisher to determine the required vertical speed in FPM, and include this as part of the approach briefing. If no angle is stated, it should be 3º.
On NACO charts, this is in the front matter of each chart book (paper), or in the Digital Terminal Procedures Supplemental (electronic). On Jeppesen charts, a table with only the descent angle for that approach is shown on the approach chart itself. Check your groundspeed (GPS/FMS/DME) once established on the approach outside the FAF to ensure you choose an appropriate descent rate.
← NACO
↑ Jeppesen

## Slide 52: Non-Precision Approach

## Slide 53: Rejected Landing
Go-around:
  Immediately and simultaneously
    Select go-around mode on flight director
    Pitch to command bars, maintain VREF minimum
    Thrust to max (stop descent)
  Establish climb VLC (around VREF)
  Flaps 20°
  Positive rate – gear up
  Flaps 12
Climb:
  At 400 feet AGL (minimum) and VREF +10 knots: flaps up
  Select appropriate flight director mode (HDG, NAV)
  Initiate missed approach procedure and advise ATC
  Accelerate to VFS / VAPP then slats up.
Complete missed approach checklist

## Slide 54: Precision Approach – One Engine Inoperative
Outside IAF:
  Airspeed 180 knots
  Complete descent and approach checks
Procedure turn outbound or base:
  Flaps 12°
  Speed 160 knots (VREF +30 knots)
  Facility tuned and identified
Localizer intercept:
  Flaps 20° (VREF +20 knots)

## Slide 55: Precision Approach – One Engine Inoperative
Approaching the final approach fix:
  One dot below glide slope
  Gear down
Final approach fix:
  Flaps remain 20°
  If electing to land flaps 20° maintain VREF +15 knots
  If electing to land flaps 40° maintain VREF +10 knots
Landing assured:
  If required flaps 40° (VREF +½ gust)
  Complete before landing checklist

## Slide 56: Missed Approach – One Engine Inoperative
Go-around:
  Immediately and simultaneously
    Select go-around mode on flight director
    Pitch to command bars, maintain VREF minimum
    Thrust to max (stop descent)
  Establish climb VLC (around VREF)
  Flaps 20°
  Positive rate – gear up
  Flaps 12
Climb:
  At 400 feet AGL (minimum) and VREF +10 knots: flaps up
  Select appropriate flight director mode (HDG, NAV)
  Initiate missed approach procedure and advise ATC
  Accelerate to VFS / VAPP then slats up
Complete missed approach checklist

## Slide 57: Circling Approach
Category for circling:
  Protected airspace (see table on next slide)
  The approach category is always based on VREF at maximum certified landing weight
  It is never permissible to use a lower approach category based on the aircraft’s actual landing weight
  Using a target speed above VREF may result in using a higher category
    VREF at 19,000 lbs. = 125 knots = Category C
    VREF+20 at 19,000 lbs. = 145 knots = Category D
  If the minima are not published, circling approaches are not permitted
Configuration:
  Gear down/ flaps 20° at FAF
  Speed VREF + 20 for maneuvering (25° of bank minimum not to exceed 30°)
  Landing assured: flaps 40° and VREF +½ gust
Crew coordination:
  Report leaving MDA
  Use of flight director and altitude select
  Procedure in the event of a missed during a circle

## Slide 58: Use Circling Minimums
NACO Example
Jeppesen Example
Circling MDA in feet MSL | Approach Category and Circling Radius (NM) |  |  |  | 
 | CAT A | CAT B | CAT C | CAT D | CAT E
1000 or less | 1.3 | 1.7 | 2.7 | 3.6 | 4.5
1001-3000 | 1.3 | 1.8 | 2.8 | 3.7 | 4.6
3001-5000 | 1.3 | 1.8 | 2.9 | 3.8 | 4.8
5001-7000 | 1.3 | 1.9 | 3.0 | 4.0 | 5.0
7001-9000 | 1.4 | 2.0 | 3.2 | 4.2 | 5.3

## Slide 59: No-Flap or Nonstandard-Flap Approach
Flap unbalance:
  Do not move flap handle
  Use checklist for no-flaps landing
No-flaps landing:
  Use chart for Abnormal Flaps/Slats Configuration for new VREF
  Increase landing distance approximately 30%
  Maintain 160 knots or new VREF +20 for maneuvering prior to final
  Use new VREF + ½ gust on final
  Do not deploy reversers until nose wheel is firmly on runway

## Slide 60: No-Flap or Nonstandard-Flap Approach
Slat failure or unbalance:
  Push SLAT BYPASS ARM button
  Flaps no greater than 20
  Increase landing distance approximately 30%
No-slats/no-flaps landing:
  Max landing weight is 18,000 lbs
  Increase landing distance approximately 50%
For all abnormal slat/flap configurations:
  Do not press HORN OFF pushbutton
  Push FLAP OVERRIDE on final
  Flare is not recommended

## Slide 61: No-Flap or Nonstandard-Flap Approach

## Slide 62: Landing with Pitch Mistrim
Elevator control failure:
  Pitch is now controlled with horizontal stabilizer trim
  Small corrections in pitch can be achieved with normal trim, larger changes with emergency trim
  Visual conditions is recommended
  Use of an approach with vertical guidance is recommended
  Establish a long, flat final to allow time to stabilize between configuration changes
  Flaps 20° maximum, VREF +15
  Note:
    Power increase causes nose-down pitch
    Power decrease causes nose-up pitch

## Slide 63: Windshear During Approach/Landing
Recognize:
    Airspeed trend indicator/AOA
    Winds increasing during descent
    Groundspeed & wind direction vs. reported winds
    Unusual thrust settings
    Unusual pitch attitudes
    GPWS/LLWAS
React:
    Verify maximum power (APR?)
    Pitch initially to 15°
    Pitch to maintain positive climb or stop descent
    Do not change configuration until sustained climb and 1000 feet above obstacles
    Normal missed approach procedures
Report:
    Advise ATC of deviations

## Slide 64: Visual Approach
Pattern entry:
  Flaps 20° VREF +20 knots
Abeam numbers:
  Gear down, Before Landing checklist
Final turn:
  VREF +20 knots
Landing assured:
  Flaps 40°
  Autopilot / Yaw Damp disconnected
  VREF +½ gust

## Slide 65: Visual Approach

## Slide 66: Engine Failure – Shutdown & Restart
Identify and verify failure:
  Engine gauges
  Annunciator lights
  Rudder inputs
Evaluate restart:
  If internal mechanical failure, do not attempt restart
  If engine fire, do not attempt restart
Checklists:
  Engine Shutdown In Flight
  Windmilling Air-start or Starter Assisted Air-start
Confirm each action
Advise ATC and consider diversion

## Slide 67: Navigation & Avionics Failures
DPU/MPU and CRT failures:
  Switches located on console
    CRT Failures:
      Press ADI (information composited on ADI)
      Press HSI (information composited on HSI)
    DPU Failure:
      Press DPU FAIL (uses MPU to generate symbol)
      For radar, use HSI sector modes
EFIS input failures:
  Switches located on panel, press switch for cross-side data
    EFIS 86 airplanes: autopilot may be lost
    EFIS 85 airplanes: autopilot may be restored

## Slide 68: Anti-Ice & De-Ice Systems
Anti-ice:
  Engine anti-ice:
    On when +5C or less and visible moisture
    At +10C or above, 10 seconds per engine during ground check when icing conditions do not exist
  Probes heat:
    OVRRD position of the probe heat switch should not be used for longer than 30 seconds on the ground
Surface de-ice:
  Do not use if:
    Temperature is -40C or below
    SURF DE-ICE light on
    Visible failure of the system

## Slide 69: Anti-Ice & De-Ice Systems
Nacelle Anti-icing Schematic

## Slide 70: Anti-Ice & De-Ice Systems
Windshield Heating System Schematic

## Slide 71: Anti-Ice & De-Ice Systems
Surface De-ice Schematic

## Slide 72: Fuel System
Basic fuel system abnormal considerations:
  Fuel jettison:
    Stops automatically when associated wing reaches 600 lbs.
    One jettison valve fails to close (no pump / no dump)
    One jettison valve fails to open (fuel balancing)
  Fuel balancing:
    Maximum imbalance during any phase of flight: 800 lbs.
    Open interconnect (kick the fuel / fuel follows the ball)
    If engine inoperative, standby pump must be ON
  Fuel low:
    Either collector box not full, -or- 450 lbs. or less in either wing
    Interconnect (consider)
    If quantity reaches 200 lbs., turn standby pumps on

## Slide 73: Fuel System
Fuel Distribution

## Slide 74: Fuel System
Fuel System Valves and Float Switches

## Slide 75: Fuel System
Engine Fuel System

## Slide 76: Electrical System
DC Electrical:
  Failure of one generators:
    Consider starting APU if so equipped
    Consider diversion
  Failure of two generators:
    Do not start APU
    Generator reset.
    Time remaining on batteries vs. time to get it on the ground.
    Battery master: VMC vs. IMC
    Slats/flaps
AC Electrical:
  Inverter failure:
    EFIS 85 – Avionics (flight instruments)
    EFIS 86 – Fans

## Slide 77: Hydraulic System
Failure of main system:
  Systems lost:
    Nose wheel steering
    Flight airbrakes and Ground airbrakes
    Normal brakes
    Normal landing gear extension
Failure of auxiliary system:
  Systems lost:
    Normal thrust reversers (with accumulator – ½ cycle)
    Parking brake / emergency brake
Total failure of hydraulic system:
  Down to auxiliary accumulator only: Either ½ cycle of thrust reversers, or 10 brake applications maximum

## Slide 78: Environmental System
Bleed system malfunctions:
  In flight consider diversion
  When annunciators extinguish, STOP the checklist.
  Monitor ITT. An unusually high ITT could indicate the source of the leak.
Pressurization abnormal:
  Consider donning oxygen masks.
  Consider descent.
Manual pressurization:
  Cabin altitude cherry picker:
    INCREASE position to open outflow valves
    DECREASE position to close outflow valves
  Cabin rate:
    Selects how fast the cabin will change in the selected direction

## Slide 79: Environmental System
Pneumatic Manifold

## Slide 80: Environmental System
Flight Operations Heating

## Slide 81: Environmental System
Automatic Operation

## Slide 82: Fire Detection & Extinguishing
Engine fire/overheat below V1:
  Overheat:
    Abort
    Thrust lever – cutoff
    Illuminated FIRE/OVERHT pushbutton – press
    Motor engine
  Fire:
    Abort
    Thrust lever – cutoff
    Illuminated FIRE/OVERHT pushbutton – press
    Engine start switch – press STOP if required
    ARM/EMPTY pushbutton – press
    Evacuation

## Slide 83: Fire Detection & Extinguishing
Engine fire above V1:
  During takeoff:
    Continue takeoff to safe altitude
  During flight:
    Thrust lever idle (at safe altitude)
    Thrust lever – cutoff
    Illuminated FIRE/OVERHT pushbutton – press
    IF FIRE remains illuminated: ARM/EMPTY pushbutton – press
    Consider diversion
    Checklist

## Slide 84: Fire Detection & Extinguishing
Engine Fire-Extinguishing Schematic

## Slide 85: Flight Controls
Aileron failure:
  Servo actuator failure:
    AILERON FAIL light indicates mechanical failure in one or both hydraulic servo actuators
    Auxiliary hydraulic system comes on automatically to power the redundant aileron actuator
  Jammed aileron:
    Apply sufficient pressure on aileron mechanical system to break interconnect
    Only one aileron will operate
  Total loss of aileron power control:
    Mechanical system operates ailerons (expect higher than normal control forces)
    Reduce speed; Autopilot should be available up to 250 knots

## Slide 86: Rapid Decompression
Immediate action items:
  PF & PM: Crew oxygen masks – don & checked 100%
  PF & PM: Crew communication – established
  PM: Seatbelt/no smoke sign – ON
  PM: Passenger oxygen controls – Both ON (switch & bypass valve); ensure passengers are receiving oxygen
  PF: Execute emergency descent
  PM: Cabin Air selector – EMER
  PM: Transponder – 7700

## Slide 87: Emergency Descent
Pilot flying actions:
  Oxygen masks – as required
  Autopilot – disengage
  Thrust levers – idle
  Flight airbrakes – extend
  Bank – 45° to 60°
  Pitch – establish descent (7° initially, don’t exceed 15°)
  Roll wings level and return heading to parallel previous course
  Communicate and call for checklist
  Maintain MMO/VMO
  Level off altitude – determine
  2000 before level off – pitch to 5° nose down
  500 before level off – retract flight airbrakes

## Slide 88: Emergency Descent
Pilot monitoring actions:
  Oxygen masks – as required
  Seat belt/no smoking signs – on
  Passenger oxygen selector – on (switch & bypass valve) if required
  Cabin air selector – EMERGency (situational dependent)
  Transponder – 7700
  Communicate – crew & ATC
  Checklist – accomplish
  Monitor cabin altitude

## Slide 89: In-Flight Fire & Smoke
Cockpit or cabin fire/smoke:
  Crew oxygen masks – don and checked (100% & continuous flow)
    Vent valve – open (pull down) if so equipped
  Smoke goggles – on
    (Glasses ON/OFF; headsets ON/OFF)
  Crew communications – established
    Hot Mic / MASK selected / headsets on
    How do you communicate with each other/ATC?
  Cabin lights switch – BELTS / NO SMOKE
  Passenger oxygen switch & bypass valve – both on
How do you find the source?
How do you extinguish?
Smoke extraction

## Slide 90: Emergency Evacuation
Window exits:
  Procedure:
    Red release handle – pull
    Window falls inward
    Throw outside to free exit
  Considerations:
    Ground airbrakes position, flaps position
Main entrance/exit:
  Procedure:
    Who evacuates the passengers?
    Pressure relief for door?
  Considerations:
    Where do passengers go?
    Emergency services/ runway closure

## Slide 91: Training Program Overview
Session 1
Session 6
Session 2
Session 3
Session 4
Session 5
Session 1
Session 2
Session 3
EASA
Session 7 (LOST)
RECURRENT (TCE)
INITIAL
Notes: Slide Title:
LESSON ORGANIZATION
Instructor Actions:
Content:
References:
Simulation State:
Malfunctions:

## Slide 92: ASTRA Initial (Sim 1)
Preflight Procedures
Preflight Inspection (Cockpit Only) (S)
Powerplant Start – Normal
Taxiing/Runway Operations
Pretakeoff Checks (S)
Auxiliary Power Unit Start - Normal
Takeoff and Departure Phase
Normal Takeoff (S)
Departure Procedure
Inflight Maneuvers
Steep Turns
Approach to Stall, Clean Configuration
Approach to Stall, Takeoff or Approach Configuration
Approach to Stall, Landing Configuration
Recovery from Unusual Attitudes
Instrument Procedures
Standard Terminal Arrival/FMS Procedures
Holding
Precision Approach, All Engines Operating
Missed Approach from Precision Approach
Visual
Landings and Approaches to Landings
Normal Landing (S)
Landing from a Precision Approach (S)
Rejected Landing
Normal and Abnormal Procedures
Navigation and Avionics Systems
Automatic Flight Control System, Electronic Flight Instrument System & Related Subsystems
Postflight Procedures
After-Landing Procedures
Parking and Securing
Notes: Slide Title:
LESSON OBJECTIVES
Instructor Actions:
Content:
References:
Simulation State:
Malfunctions:

## Slide 93: ASTRA Initial (Sim 2)
Preflight Procedures
Preflight Inspection (Cockpit Only) (S)
Powerplant Start – Normal
Powerplant Start – Abnormal
Pretakeoff Checks (S)
Auxiliary Power Unit Start – Abnormal
Takeoff and Departure Phase
Normal Takeoff (S)
Crosswind Takeoff (S)
Departure Procedure
Inflight Maneuvers
Powerplant Failure (Including Shutdown and Restart)
Powerplant Failure (Including Shutdown and Restart, and maneuvering with an Engine Out while executing the duties of Pilot-In-Command) (S)
Instrument Procedures
Holding
Nonprecision Approach 1 (S)
Nonprecision Approach 2
Circling Approach
Missed Approach from a Non-precision
Visual
Landings and Approaches to Landings
Normal Landing (S)
Crosswind Landing (S)
Landing from a Circling Approach
Rejected Landing
Normal and Abnormal Procedures
Powerplant
Fuel System
Electrical System
Automatic Flight Control System, Electronic Flight Instrument System & Related Subsystems
Flight Control Systems
Aircraft & Personal Emergency Equipment
Auxiliary Power Unit Fire
Postflight Procedures
After-Landing Procedures
Parking and Securing
Notes: Slide Title:
LESSON OBJECTIVES
Instructor Actions:
Content:
References:
Simulation State:
Malfunctions:

## Slide 94: ASTRA Initial (Sim 3)
Preflight Procedures
Pretakeoff Checks (S)
Auxiliary Power Unit Start - Normal
Takeoff and Departure Phase
Crosswind Takeoff (S)
Powerplant Failure During Takeoff
Rejected Takeoff (S)
Departure Procedure
Instrument Procedures
Precision Approach, One Engine Inoperative
Nonprecision Approach 2
Circling Approach
Missed Approach with a Powerplant Failure
Landings and Approaches to Landings
Approach and Landing with a Powerplant Failure (S)
Normal and Abnormal Procedures
Powerplant
Electrical System
Fire Detection and Extinguishing Systems
Postflight Procedures
After-Landing Procedures
Parking and Securing
Notes: Slide Title:
LESSON OBJECTIVES
Instructor Actions:
Content:
References:
Simulation State:
Malfunctions:

## Slide 95: ASTRA Initial (Sim 4)
Preflight Procedures
Pretakeoff Checks (S)
Takeoff and Departure Phase
Normal Takeoff (S)
Crosswind Takeoff (S)
Instrument Takeoff
Departure Procedure
Instrument Procedures
Nonprecision Approach 1 (S)
Nonprecision Approach 2
Missed Approach from a Non-Precision
Landings and Approaches to Landings
Normal Landing (S)
Crosswind Landing (S)
Rejected Landing
Normal and Abnormal Procedures
Fuel System
Electrical System
Environmental System
Pressurization System
Anti-ice and Deice Systems
Emergency Procedures
Inflight Fire and Smoke Removal
Emergency Evacuation
Airframe Icing
Postflight Procedures
After-Landing Procedures
Parking and Securing
Notes: Slide Title:
LESSON OBJECTIVES
Instructor Actions:
Content:
References:
Simulation State:
Malfunctions:

## Slide 96: ASTRA Initial (Sim 5)
Preflight Procedures
Pretakeoff Checks (S)
Takeoff and Departure Phase
Normal Takeoff (S)
Departure Procedure
Inflight Maneuvers
Power Off Stall Demonstration
Instrument Procedures
Nonprecision Approach 1 (S)
Landings and Approaches to Landings
Normal Landing (S)
Landing from a No Flap or a Nonstandard Flap Approach
Normal and Abnormal Procedures
Hydraulic System
Environmental System
Pressurization System
Flight Control Systems
Landing Gear and Brakes
Emergency Procedures
Emergency Descent (Maximum Rate)
Rapid Decompression
Postflight Procedures
After-Landing Procedures
Parking and Securing
Notes: Slide Title:
LESSON OBJECTIVES
Instructor Actions:
Content:
References:
Simulation State:
Malfunctions:

## Slide 97: ASTRA Initial (Sim 6 )
Preflight Procedures
Preflight Inspection (Cockpit Only) (S)
Powerplant Start – Normal
Power plant Start – Abnormal
Taxiing/Runway Operations
Pretakeoff Checks (S)
Auxiliary Power Unit Start – Normal
Takeoff and Departure Phase
Normal Takeoff (S)
Crosswind Takeoff (S)
Instrument Takeoff
Powerplant Failure During Takeoff
Rejected Takeoff (S)
Departure Procedure
Inflight Maneuvers
Steep Turns
Approach to Stall, Clean Configuration
Approach to Stall, Takeoff or Approach Configuration
Approach to Stall, Landing Configuration
Powerplant Failure (Including Shutdown and Restart)
Powerplant Failure (Including Shutdown and Restart, and maneuvering with an Engine Out while executing the duties of Pilot-In-Command) (S)
Recovery from Unusual Attitudes
Instrument Procedures
Standard Terminal Arrival/FMS Procedures
Holding
Precision Approach, All Engines Operating
Precision Approach, One Engine Inoperative
Nonprecision Approach 1 (S)
Nonprecision Approach 2
Circling Approach
Missed Approach from Precision Approach
Missed Approach with a Powerplant Failure
Visual
Landings and Approaches to Landings
Normal Landing (S)
Crosswind Landing (S)
Landing from a Precision Approach (S)
Approach and Landing with a Powerplant Failure (S)
Landing from a Circling Approach
Rejected Landing
Landing from a No Flap or a Nonstandard Flap Approach
Normal and Abnormal Procedures
Powerplant
Fuel System
Electrical System
Hydraulic System
Fire Detection and Extinguishing Systems
Automatic Flight Control System, Electronic Flight Instrument System and Related Subsystems
Flight Control Systems
Postflight Procedures
After-Landing Procedures
Parking and Securing
Notes: Slide Title:
LESSON OBJECTIVES
Instructor Actions:
Content:
References:
Simulation State:
Malfunctions:

## Slide 98: ASTRA Initial (Sim 7 - LOST)
Line-Oriented Simulation Training (LOST) will facilitate the transition from practicing specific maneuvers in the Flight Simulator Modules to integration of all applicable maneuvers into a simulated total flight. LOST will include two (2) flight segments.
Segment One
  This segment includes strictly normal procedures from taxi after engine start at one airport, to arrival at another.
Segment Two
  This segment includes training in appropriate abnormal and emergency flight operations.
Notes: Slide Title:
LESSON OBJECTIVES
Instructor Actions:
Content:
References:
Simulation State:
Malfunctions:

## Slide 99: ASTRA Recurrent - TCE (Sim 1)
Preflight Procedures
Pre-Flight Inspection (Cockpit Only) (S)
Powerplant Start – Normal
Powerplant Start – Abnormal
Taxiing/Runway Operations
Pretakeoff Checks (S)
Takeoff and Departure Phase
Normal Takeoff (S)
Crosswind Takeoff (S)
Instrument Takeoff
Departure Procedure
Inflight Maneuvers
Steep Turns
Approach to Stall, Clean Configuration
Approach to Stall, Takeoff or Approach Configuration
Approach to Stall, Landing Configuration
Powerplant Failure (Including Shutdown & Restart)
Powerplant Failure (Including Shutdown & Restart, and maneuvering with an Engine Out while executing the duties of Pilot-In-Command) (S)
Recovery from Unusual Attitudes
Instrument Procedures
Standard Terminal Arrival/FMS Procedures
Holding
Precision Approach, One Engine Inoperative
Missed Approach from Precision Approach
Missed Approach with a Powerplant Failure
Landings and Approaches to Landings
Normal Landing (S)
Landing from a Precision Approach
Approach and Landing with a Powerplant Failure (S)
Normal and Abnormal Procedures
Powerplant
Anti-ice and Deice Systems
Aircraft and Personal Emergency Equipment
Postflight Procedures
After-Landing Procedures
Parking and Securing
Notes: Slide Title:
LESSON OBJECTIVES
Instructor Actions:
Content:
References:
Simulation State:
Malfunctions:

## Slide 100: ASTRA Recurrent - TCE (Sim 2)
Preflight Procedures
  Pretakeoff Checks (S)
Takeoff and Departure Phase
  Normal Takeoff (S)
  Crosswind Takeoff (S)
  Powerplant Failure During Takeoff
  Rejected Takeoff (S)
Instrument Procedures
  Non-precision Approach 1(S)
  Non-precision Approach 2
  Circling Approach
  Visual
Landings and Approaches to Landings
  Crosswind Landing (S)
  Landing from a Circling Approach
  Rejected Landing
  Landing from a No Flap or a Nonstandard Flap Approach
Normal and Abnormal Procedures
  Fuel System
  Fire Detection and Extinguishing Systems
  Navigation and Avionics Systems (S)
  Automatic Flight Control System, Electronic Flight Instrument System and Related Subsystems
  Flight Control Systems
Postflight Procedures
  After-Landing Procedures
  Parking and Securing
Notes: Slide Title:
LESSON OBJECTIVES
Instructor Actions:
Content:
References:
Simulation State:
Malfunctions:

## Slide 101: ASTRA Recurrent - TCE (Sim 3)
Preflight Procedures
  Pre-takeoff Checks (S)
Takeoff and Departure Phase
  Crosswind Takeoff (S)
  Windshear
Instrument Procedures
  Visual
Landings and Approaches to Landings
  Normal Landing (S)
  Windshear
Normal and Abnormal Procedures
  Electrical System
  Hydraulic System
  Environmental System
Emergency Procedures
  Emergency Descent (Maximum Rate)
  Inflight Fire and Smoke Removal
  Rapid Decompression
  Emergency Evacuation
Postflight Procedures
  After-Landing Procedures
  Parking and Securing
Notes: Slide Title:
LESSON OBJECTIVES
Instructor Actions:
Content:
References:
Simulation State:
Malfunctions:

## Slide 102: Profiles and Maneuvers
Standard Takeoff Procedure
Rejected Takeoff
Engine Failure During Takeoff
Stall Recovery: Clean Configuration
Stall Recovery: Takeoff Partial Flaps
Stall Recovery: Landing Configuration
Precision Approach
Missed Approach
Non-Precision Approach
Approach – No Flaps
Visual Approach

## Slide 103: Astra Initial
Session 1:
Engine Start – Normal
Taxi
Standard Takeoff
Normal Climb
Trim & Pitch Change Characteristics
Precision Approach
Normal Landing
Session 2:
Engine Start – Normal
Engine Start – Abnormal
Steep Turns
Stall (Clean Configuration)
Stall (Departure Configuration)
Stall (Landing Configuration)
In-flight Shutdown and Restart
Flight Controls
Missed Approach from Precision
Non-Precision Approach
Rejected Landing
Visual Approach
Session 3:
Rejected Takeoff
Engine Failure at V1 during Takeoff
Precision Approach – OEI
Missed Approach – OEI
Unusual Attitudes
Circling Approach
Missed Approach from Non-Precision
Navigation / Avionics Failure
Emergency Evacuation
Session 4:
Windshear: Takeoff
Anti-ice and De-ice Systems
Fuel System
Fire Detection and Extinguishing
Environmental / Pressurization
In-flight Fire and Smoke Removal
Stall (High Altitude)
Rapid Decompression / Emerg. Descent
Windshear: Approach/Landing
No-flap or Nonstandard-flap Landing
Landing with a Pitch Mistrim
Session 5:
Steep Turns
Stall (Clean Configuration)
Stall (Departure Configuration)
Stall (Landing Configuration)
Unusual Attitudes
In-flight Shutdown and Restart
Electrical System
Hydraulic System
Circling Approach
Precision Approach and Landing – OEI
Session 6:
Steep Turns
Stall (Clean Configuration)
Stall (Departure Configuration)
Stall (Landing Configuration)
Unusual Attitudes
In-flight Shutdown and Restart
Electrical System
Hydraulic System
Circling Approach
Precision Approach and Landing – OEI
Session 7 (LOST):

## Slide 104: Astra Recurrent (TCE)
Session 1:
Engine Start – Normal
Engine Start – Abnormal
Taxi
Standard Takeoff
Normal Climb
Anti-ice / De-ice Systems
Steep Turns
Stall (Clean Configuration)
Stall (Departure Configuration)
Stall (Landing Configuration)
In-flight Shutdown & Restart
Unusual Attitudes
Precision Approach
Non-Precision Approach
Circling Approach
Missed Approach from Precision
Rejected Landing
Session 2:
Engine Failure at V1 During Takeoff
Rejected Takeoff
Precision Approach – OEI
No-flap or Nonstandard-flap Approach & Landing
Missed Approach from Non-Precision
Visual Approach
Fuel System
Environmental / Pressurization
Fire Detection and Extinguishing
Navigation / Avionics Failure
Flight Controls
In-flight Fire and Smoke Removal
Session 3:
Windshear: Takeoff
Landing with a Pitch Mistrim
Missed Approach – OEI
Windshear: Approach/Landing
Electrical System
Hydraulic System
Rapid Decompression
Emergency Descent
Emergency Evacuation